# Calc Histogram
## Description
This functor calculates a histogram from a map.
## Inputs
Name	Type	Description
Map	Map Type	Any map

## Optional Inputs
Name	Type	Description	Default Value
Interval Width	Real Value Type	The width of the histogram interval.	1.0
Cumulative	Boolean Value Type	If true, the calculated histogram is cumulative.	False
Relative	Boolean Value Type	If true, the values in the histogram are normalized by the total number of occurrences.	False

## Outputs
Name	Type	Description
Histogram	Lookup Table	The calculated histogram.

## Notes
It also possible to calculate a histogram relative to the cumulative values. To do this, set both input flags (“Cumulative” and “Relative”).
When the “Interval Width” is different from one, the input values are remapped according to the expression below to speed up the calculation.
, where value2 is the resulting value, value is the value present in the input map and width is the “Interval Width”.
Because of the remapping, the lower limit of the resulting histogram can be lower than the minimum value in the input map. The upper limit of the histogram can be greater than the maximum value in the input map.
## Group
Statistics
## Internal Name
CalcHistogram