# Create Categorical Map
## Description
This functor creates an empty map of classes or categories using the given parameters.
## Inputs
Name	Type	Description
Lines	Positive Integer Value	Number of lines.
Columns	Positive Integer Value	Number of columns.
Cell Type	Cell Type	Data cell type.
Null Value	Null Value	Null value.
Categories	Categorization	Map categories.
Projection	Projection	Map projection.
Cell Width	Real Value	Cell width.
Cell Height	Real Value	Cell height.
Registration Coordinate Y	Real Value	The registration coordinate Y. The unit used to represent the registration coordinate is based on the projection assigned. Corresponds to Northing or Latitude.
Registration Coordinate X	Real Value	The registration coordinate X. The unit used to represent the registration coordinate is based on the projection assigned. Corresponds to Easting or Longitude.

## Optional Inputs
Name	Type	Description	Default Value
Registration Cell Y	Positive Integer Value	The line of the registered coordinate. The line 1 is the topmost line.	1
Registration Cell X	Positive Integer Value	The column of the registered coordinate. The column 1 is the leftmost column.	1
Create As Sparse	Boolean Value	If true, this flag forces the map to be created as a sparse raster set. Sparse raster set stores only non-null value cells, minimizing storage memory in detriment of access time.	False

## Outputs
Name	Type	Description
Map	Categorical Map	The output map of classes or categories.

## Group
Map Algebra
## Notes
All map cells are initialized with the specified null value.
## Internal Name
CreateCategoricalMap