# Extract Lookup Table Attributes
## Description
This functor extracts attributes and summary statistics from a lookup table.
## Inputs
Name	Type	Description
Table	Lookup Table Type	A lookup table.

## Optional Inputs
Name	Type	Description	Default Value
Extract Statistical Key Attributes	Boolean Value Type	If true, the calculation includes statistical key attributes (items 10-16).	True
Extract Statistical Value Attributes	Boolean Value Type	If true, the calculation includes statistical value attributes (items 20-26).	False
Extract Dynamic Key Value Attributes	Boolean Value Type	If true, the calculation includes statistical value attributes (items 30-32).	False

## Outputs
Name	Type	Description
Attributes	Lookup Table Type	Table containing the attributes extracted from a table.

## Group
Table
## Notes
The functor employs a lookup table with keys to the attributes. Each key has a predefined name. This name can be used to retrieve the corresponding attribute in Calculate Map, Calculate Categorical Map, Calculate Value and Calculate Lookup Table
### Basic Attributes
Key	Predefined Name	Description
1	“uniqueKeys”	number of unique keys (lines)

### Statistical Key Attributes
<note important>The value mapped to the key by each key/value pair is used as the number of key occurrences. Keys associated with negative or zero values are supposed not be presented in the table when the key attributes are being calculated and the corresponding keys are ignored. If you do not want the value associated with the key to the used as the number of key occurrences, use a Calculate Lookup Table to turn the associated values into zeros and run the attribute calculation on the resulting table. The expression “1” can be used to turn all values into zeros before performing the attribute calculation. </tip>
Key	Predefined Name	Description
10	“minKey”	minimum key
11	“maxKey”	maximum key
12	“meanKey”	mean key
13	“modeKey”	mode key
14	“keyVar”	key variance
15	“keyStd”	key standard deviation
16	“medianKey”	median key

### Statistical Value Attributes
Key	Predefined Name	Description
20	“minValue”	minimum value
21	“maxValue”	maximum value
22	“meanValue”	mean value
23	“modeValue”	mode value
24	“valueVar”	value variance
25	“valueStd”	value standard deviation
26	“medianValue”	median value

### Dynamic Key & Value Attributes
Key	Predefined Name	Description
30	“keySum”	key sum (values are ignored)
31	“valueSum”	value sum
32	“keyValueProdSum”	sum of key/value product

If it is not possible to determine any of those attributes, the corresponding entry in the lookup table is left blank.
## Internal Name
ExtractLookupTableAttributes