# Image Expression Type
List of mathematical and logical operators that can be employed in the logic/algebraic expression.
## GUI Editor
## Operators
In the syntax tables below, EXPR denotes any arbitray expression, IMAGE denotes any image identifier (a image identifier uses the syntax iX where X is an integer value from 1 to 100), TABLE denotes any table identifier (a table identifier uses the syntax tX where X is an integer value from 1 to 100) and VALUE denotes any value identifier (a value identifier uses the syntax vX where X is an integer value from 1 to 100).

During logical expressions evaluation, a zero value is supposed to be false and a non-zero value supposed to be true.

### General Operators
Precedence	Operator	Description	Syntax	Usage Example
1	Conditional	Execute the second or third term of the equation conditionally to the first	if@@@EXPR@@@then@@@EXPR@@@else@@@EXPR	if@@@@@@not@@@@@@isNull(i1)@@@@@@and@@@@@@isNull(i2)@@@@@@then @@@@@@i3 else@@@@@@if@@@@@@isNull(i1)@@@@@@then @@@@@@i1@@@@@@–@@@@@@i1@@@@@@/@@@@@@i2 else@@@@@@(i1@@@@@@/@@@@@@i2)@@@@@@?@@@@@@(i1@@@@@@–@@@@@@i2)
2	Boolean Or	The expression evaluation returns true if any of its arguments is true. See logical disjunction for additional information about the boolean logic. The evaluation is short-circuited.	EXPR@@@or@@@EXPR EXPR@@@||@@@EXPR	not@@@@@@isNull(i1)@@@@@@or@@@@@@isNull(i2) not@@@@@@isNull(i1)@@@@@@||@@@@@@isNull(i2)
Boolean And	The expression evaluation returns true if and only if all its arguments are true. See logical conjunction for additional information about the boolean logic. The evaluation is short-circuited.	EXPR@@@and@@@EXPR EXPR@@@&&@@@EXPR	not@@@@@@isNull(i1)@@@@@@and@@@@@@isNull(i2) not@@@@@@isNull(i1)@@@@@@&&@@@@@@isNull(i2)
3	Equal		EXPR@@@=@@@EXPR EXPR@@@==@@@EXPR	i1@@@@@@=@@@@@@2 i1@@@@@@==@@@@@@2
Not Equal		EXPR@@@!=@@@EXPR EXPR@@@/=@@@EXPR EXPR@@@<>@@@EXPR	i1@@@@@@!=@@@@@@2 i1@@@@@@/=@@@@@@2 i1@@@@@@<>@@@@@@2
4	Greater Than		EXPR@@@>@@@EXPR	i1@@@@@@>@@@@@@2
Greater Than Or Equal		EXPR@@@>=@@@EXPR	i1@@@@@@>=@@@@@@2
Less Than		EXPR@@@<@@@EXPR	i1@@@@@@<@@@@@@i2
Less Than Or Equal		EXPR@@@<=@@@EXPR	i1@@@@@@<=@@@@@@i2
5	Add		EXPR@@@+@@@EXPR	i1@@@+@@@i2
Subtract		EXPR@@@–@@@EXPR	i1@@@–@@@i1@@@/@@@i2
6	Times		EXPR@@@*@@@EXPR	i1@@@*@@@i2
Divide		EXPR@@@/@@@EXPR	i1@@@/@@@i2
Mod		EXPR@@@%@@@EXPR	i1@@@%@@@100
7	Power		EXPR@@@^@@@EXPR	i1@@@^@@@3
8	Catch Error	Catch an algebraic error (such as division by zero, table key not found etc) and replace it with the result of another expression	EXPR@@@?@@@EXPR	(i1@@@/@@@i2)@@@?@@@(i1@@@–@@@i2)
9	Boolean Not	Return true, if its argument is false, and false, otherwise. See boolean negation for additional information about the boolean logic.	!@@@EXPR not@@@EXPR	not@@@isNull(i1) !@@@isNull(i1)
Negate		–@@@EXPR	–@@@ceil(i1@@@+@@@i2)

### General Functions
Operator	Description	Syntax	Usage Example
Value			2@@@+@@@i1@@@/@@@-3.5e-2
Random	Generate a random value using the Uniform probability distribution	rand	if@@@rand@@@>@@@0.5@@@then@@@1@@@else@@@i2
Uniform	Generate a random value using the Uniform probability distribution. The generated value lies between the given bounds. The first EXPR represents the lower bound and the second EXPR represents the upper bound	rUniform(EXPR,@@@EXPR)	if@@@rUniform(12,@@@15)@@@>@@@14@@@then@@@1@@@else@@@i2
Normal	Generate a random value using the Normal probability distribution. The value is generated according to the first and second given EXPR representing, respectively, the mean and the deviation of the distribution	rNormal(EXPR,@@@EXPR)	if@@@rNormal(10,@@@2)@@@>@@@9@@@then@@@1@@@else@@@i2
Poisson	Generate a random value using the Poisson probability distribution. The value is generated according to the given EXPR representing the distribution lambda	rPoisson(EXPR)	if@@@rPoisson(100)@@@>@@@95@@@then@@@1@@@else@@@i2
Squared Root		sqrt(EXPR)	sqrt(i1@@@/@@@i4)
Sin	Sin (input in radians)	sin(EXPR)	sin(i1@@@/@@@i4)
Cos	Cos (input in radians)	cos(EXPR)	cos(i1@@@+@@@i2)
Tan	Tan (input in radians)	tan(EXPR)	tan(i1@@@*@@@i5@@@+@@@6)
Acos	Acos (output in radians)	acos(EXPR)	acos(i1@@@+@@@i2)
Asin	Asin (output in radians)	asin(EXPR)	asin(i1@@@+@@@i2)
Atan	Atan (output in radians)	atan(EXPR)	atan(i1@@@+@@@i2)
Ceil	Convert the value to the smallest following integer	ceil(EXPR)	ceil(i1@@@+@@@i2)
Exp		exp(EXPR)	exp(i1[i1@@@+@@@i2])
Floor	Convert the value to the largest previous integer	floor(EXPR)	floor(i1@@@+@@@i2)
Round	Convert the value to the nearest integer	round(EXPR)	round(i1@@@/@@@i4)
Abs		abs(EXPR)	abs(i1@@@+@@@i2)
Ln		ln(EXPR)	ln(i1@@@/@@@i4)
Log		log(EXPR)	log(i1@@@/@@@i4)
Max		max(EXPR,@@@EXPR)	max(i1,@@@i2)
Min		min(EXPR,@@@EXPR)	min(i1,@@@i4)
Signal	Return +1, if the expression is positive, -1, if it is negative, and 0, otherwise.	signal(EXPR)	signal(i1@@@-@@@4)
Abort	Abort the model execution	abort	if@@@i1@@@>@@@0@@@then@@@i1@@@*@@@i2@@@+@@@4@@@else@@@abort
Pi	Return the value of the constant Π (3.14159265358979323846)	pi	i1@@@*@@@pi@@@/@@@180
Clamp	Clamp the value to a specified range. The first EXPR represents the value that will be clamped. The second and third EXPR represent the minimum and the maximum value from the range used to clamp the given value. This function is equivalent to the following expression: @@@@@@if@@@EXPR@@@<@@@EXPR_MIN@@@then @@@@@@@@@@@@EXPR_MIN @@@@@@else@@@if@@@EXPR@@@>@@@EXPR_MAX@@@then @@@@@@@@@@@@EXPR_MAX @@@@@@else @@@@@@@@@@@@EXPR	clamp(EXPR,@@@EXPR,@@@EXPR)	clamp(v1, 1, 12)
ClampMod	Clamp the value to a specified range, but use the mod of the range to determine where the given value lies in. The first EXPR represents the value that will be clamped. The second and third EXPR represent the minimum and the maximum value from the range used to clamp the given value. This function is approximately equivalent to the following expression: @@@@@@if@@@EXPR@@@>@@@EXPR_MAX@@@or@@@EXPR@@@<@@@EXPR_MIN@@@then @@@@@@@@@@@@(EXPR@@@-@@@EXPR_MIN)@@@%@@@(EXPR_MAX@@@-@@@EXPR_MIN@@@+@@@1)@@@+@@@EXPR_MIN@@@-@@@1 @@@@@@else @@@@@@@@@@@@EXPR	clampMod(EXPR,@@@EXPR,@@@EXPR)	clampMod(v1, 2010, 2054)

### Value Operators
Operator	Description	Syntax	Usage Example
Get Variable Value	Return the variable value	vX where X is an integer value from 1 to 100	v1@@@+@@@t1[v2@@@+@@@4]

### Image Operators and Functions
Operator	Description	Syntax	Usage Example
Get Image Value	Return the image value at the current cell	IMAGE	i2
Get Image Value At Location	Return the image value on the specified cell coordinate. The cell coordinate is defined by two expressions where the first expression represents the cell line and the second expression represents the cell column.	IMAGE[@@@,@@@]	i1[line@@@–@@@1,@@@column@@@–@@@2]
Get Image Null Value	Return the null value of the current image. It is also possible to specify an image whose corresponding null value will be retrieved. The use of null without specifying an image “poisons” the expression evaluation forcing the expression result to be invalid.	null null(IMAGE)	if@@@i1@@@>@@@2@@@then@@@i1@@@else@@@null if@@@null(i2)@@@>@@@2@@@then@@@1@@@else@@@null
Is Null	Return 1, if the given expression is null, and 0, otherwise. Can also be used to test whether the result of any expression is invalid or not.	isNull(EXPR)	if@@@not@@@isNull(i1)@@@then@@@i1@@@else@@@i2
Get Line Number	Return the line number of the current cell	line	line@@@+@@@1
Get Column Number	Return the column number of the current cell	column	if column@@@/@@@2@@@>@@@50@@@then@@@1@@@else@@@null

### Lookup Table Operators
Lookup table operators return the value corresponding to a given key according to a rule-operator.
They have the following syntax:
@@@@@@@@@TABLE[N@@@]
where:
@@@@@@@@@TABLE is a table identifier corresponding to a lookup table. Beware that, if the identifier corresponds to a table, an error will be reported;
@@@@@@@@@N is the rule-operator.
Operator	Description	Syntax	Usage Example
Get Table Value	Return the table value in the X key position of the table	TABLE[EXPR]	t2[i1@@@+@@@2]
Get Table Equal Lower Bound Value	Return the table value in the greater key less than or equal to the X key position of the table.	TABLE[<=@@@EXPR] TABLE{EXPR}	t2[<=@@@14] t2{14}
Get Table Lower Bound Value	Return the table value in the greater key less than the X key position of the table.	TABLE[<@@@EXPR]	t2[<@@@i1@@@+@@@2]
Get Table Equal Upper Bound Value	Return the table value in the lesser key greater than or equal to the X key position of the table.	TABLE[>=@@@EXPR]	t2[>=@@@i1@@@+@@@i3]
Get Table Upper Bound Value	Return the table value in the lesser key greater than the X key position of the table.	TABLE[>@@@EXPR]	t2[>@@@i7]
Get Table Closest Value	Return the table value in the key closest to the X key position of the table.	TABLE[><@@@EXPR]	t2[><@@@3@@@+@@@i7]
Get Table Interpoled Value	Return a linear interpoled value drawn through the neighbor keys of the X key position of the table.	TABLE[/@@@EXPR]	t2[/@@@i2]
Test Table Key	Return 1, if expression corresponds to a key stored in the table, and 0, otherwise.	TABLE[?@@@EXPR] TABLE[=?@@@EXPR] TABLE[==?@@@EXPR]	t2[?@@@i2] t2[=?@@@i2]
Get Table Value Using Predefined Name	Return the table value bound to a key corresponding to a predefined name. This can only used to retrieve results produced by Extract Map Attributes e Extract Lookup Table Attributes. The documentation of these operators provides a list of all supported predefined names.	TABLE[“NAME”]	t2[“cellArea”]

### Table Operators
Table operators return the value corresponding to a given set of keys.
They have the following syntax:
@@@@@@@@@TABLE[@@@[@@@]@@@[@@@]@@@]
where:
@@@@@@@@@TABLE is a table identifier corresponding to a table. Beware that, if the identifier corresponds to a lookup table, an error will be reported;
The expressions representing the set of keys must be separated by commas.
Operator	Description	Syntax	Usage Example
Get Table Value At Default Column	Return the table value corresponding to the set of keys at the first data column.	TABLE[@@@[EXPR,@@@EXPR,@@@EXPR,@@@...@@@]@@@]	t2[@@@[i1@@@+@@@2,@@@i2/2,@@@t1[v2]]@@@]
Get Table Value At Named Column	Return the table value corresponding to the set of keys at the column named by the given name.	TABLE[@@@[EXPR,@@@EXPR,@@@EXPR,@@@...@@@]@@@[@@@NAME@@@]@@@]	t2[@@@[i1@@@+@@@2,@@@i2/2,@@@t1[v2]]@@@[@@@“Area_In_Hectares”@@@]@@@]
Get Table Value At Column Index	Return the table value corresponding to the set of keys at the column indexed by the given expression.	TABLE[@@@[EXPR,@@@EXPR,@@@EXPR,@@@...@@@]@@@[@@@EXPR@@@]@@@]	t2[@@@[i1@@@+@@@2,@@@i2/2,@@@t1[v2]]@@@[@@@v1+2@@@]@@@]

### Image Neighborhood Functions
Neighborhood operators return the value of an operation within a defined neighborhood window.
They have the following syntax:
@@@@@@@@@nbN(IMAGE,@@@h,@@@w,@@@y,@@@x)
where:
@@@@@@@@@N is the operator name;
@@@@@@@@@IMAGE is an image identifier;
@@@@@@@@@h is the number of window lines;
@@@@@@@@@w is the number of window columns;
@@@@@@@@@y is the line where the window center is anchored at the image;
@@@@@@@@@x is the column where the window center is anchored at the image.
The calculation usually includes the center of the window.
Even-sided windows have the center displaced toward the top left corner.

The window anchor (y and x) can be omitted when the window center is anchored at the current line and column. The shortened syntax is: @@@@@@@@@nbN(IMAGE,@@@h,@@@w)

Operator	Description	Syntax	Usage Example
Min	Returns the minimum value of the neighbor non-null cells.	nbMin()	nbMin(i4,@@@2,@@@3,@@@line-1,@@@column)
Max	Returns the maximum value of the neighbor non-null cells.	nbMax()	nbMax(i1,@@@4,@@@4)@@@-@@@1
Sum	Returns the sum of the neighbor non-null cells.	nbSum()	nbSum(i3,@@@5,@@@5)@@@+@@@7
Product	Returns the product of the neighbor non-null cells.	nbProd()	if@@@not@@@isNull(i1)@@@then@@@nbProd(i1,@@@2,@@@2,@@@0,@@@column)@@@else@@@0
Count	Returns the number of neighbor non-null cells.	nbCount()	nbCount(i2,@@@3,@@@3)@@@+@@@nbCount(i1,@@@3,@@@3,@@@line,@@@column+3)
Average	Returns the arithmetic mean of the neighbor non-null cells.	nbAverage()	round(nbAverage(i1,@@@7,@@@7))
Median	Returns the median value of the neighbor non-null cells. For an even number of values, the greater of the two median values is returned.	nbMedian()	nbMedian(i1,@@@5,@@@5)
Mode	Returns the mode of the neighbor non-null cells. If a mode does not exist, null is returned. If there is more than one, the lesser one is returned.	nbMode()	nbMode(i1,@@@5,@@@5)
Variance	Returns the variance of the values of the neighbor non-null cells according to the expression: @@@ where @@@x1, x2, ..., xi are the neighbor cells; @@@X is the mean of the neighbor cells.	nbVar()	nbVar(i4,@@@7,@@@7)@@@/@@@25
Standard Deviation	Returns the standard deviation of the neighbor non-null cells according to the expression: @@@ where @@@x1, x2, ..., xi are the neighbor cells; @@@X is the mean of the neighbor cells.	nbStdDev()	nbStdDev(i2,@@@3,@@@3,@@@line+1,@@@column)

### Image Neighborhood Indexing Functions
Neighborhood (Ref) operators finds the value of an operation within a defined neighborhood window, this value is then used as an index to retrieve data either from a table or from a secondary image.
They have the following syntax:
@@@@@@@@@nbN(IMAGE, @@@h, @@@w, TABLE, @@@y, @@@x)
@@@@@@@@@nbN(IMAGE, @@@h, @@@w, IMAGE2, @@@y, @@@x)
where:
@@@@@@@@@N is the operator name;
@@@@@@@@@IMAGE is an Image identifier;
@@@@@@@@@h is the number of window lines;
@@@@@@@@@w is the number of window columns;
@@@@@@@@@TABLE is a LookupTable containing the values associated to each Index (Key = Index);
@@@@@@@@@IMAGE2 is an Image identifier whose cell values will be returned (Cell Coordinate = Index);
@@@@@@@@@y is the line where the window center is anchored at the image;
@@@@@@@@@x is the column where the window center is anchored at the image.
The calculation usually includes the center of the window. Even-sided windows have the center displaced toward the top left corner.

The window anchor (y and x) can be omitted when the window center is anchored at the current line and column. The shortened syntax is: @@@@@@@@@nbN(IMAGE,@@@h,@@@w,@@@TABLE/IMAGE2)

Operator	Description	Syntax	Usage Example
MinRef	Finds the minimum value of the neighbor non-null cells. This value is then used as an Index to retrieve the resulting value from specified table or image.	nbMinRef()	nbMinRef(i4,@@@2,@@@3,@@@t1,@@@line,@@@column)
MaxRef	Finds the maximum value of the neighbor non-null cells. This value is then used as an index to retrieve the resulting value from specified table or image.	nbMaxRef()	nbMaxRef(i4,@@@2,@@@3,@@@i1,@@@line,@@@column)

There is one additional image neighborhood operator that uses a slightly different syntax:
@@@@@@@@@nbConvol(IMAGE,@@@TABLE,@@@h,@@@w,@@@y,@@@x)
where:
@@@@@@@@@IMAGE is an image identifier;
@@@@@@@@@TABLE is a table identifier;
@@@@@@@@@h is the number of window lines;
@@@@@@@@@w is the number of window columns;
@@@@@@@@@y is the line where the window center is anchored at the image;
@@@@@@@@@x is the column where the window center is anchored at the image.
nbConvol applies a convolution over IMAGE using the values stored on TABLE as the convolution coeficients. The table entries, from 1 to X, are mapped into the corresponding image values from top-down, left-to-right. The following examples ilustrated:
3×3 Window
1	2	3
4	5	6
7	8	9

5×5 Window
1	2	3	4	5
6	7	8	9	10
11	12	13	14	15
16	17	18	19	20
21	22	23	24	25

Like the previous definitions, the window anchor (y and x) can be omitted when the window center is anchored at the current line and column.

## EGO Script
A image expression constant can be represented in a EGO Script using the same syntax used to represent the expression in the graphical interface editor, except that it must be surrounded by [ ] (square brackets):
The following example illustrates:
[ if i1 <= (v3 - v1) / (v2 - v1) then v1 + sqrt(i1 * (v2 - v1) * (v3 - v1)) else v2 - sqrt((1 - i1) * (v2 - v1) * (v2 - v3)) ]