# Extract Map Attributes
## Description
This functor extracts the attributes and calculates basic statistics from a map and as a result creates a table that contains the extracted attributes.
## Inputs
Name	Type	Description
Map	Map	Map whose attributes will be extracted.

## Optional Inputs
Name	Type	Description	Default Value
Extract Dynamic Attributes	Bool	If true, the dynamic attributes will be calculated.	True
Extract Statistical Attributes	Bool	If true, statistical attributes will be calculated.	False

## Outputs
Name	Type	Description
Attributes	Lookup Table	Table containing the attributes extracted from a map.
Layer Attributes	Table	Table containing the layer attributes.

## Group
Map Algebra
## Notes
This functor analyzes all map layers. The resulting table refers to all of them.
The functor employs a lookup table with keys to the attributes. Each key has a predefined name. This name can be used to retrieve the corresponding attribute in Calculate Map, Calculate Categorical Map, Calculate Value and Calculate Lookup Table.
If it is not possible to determine any of these attributes, the corresponding entry in the lookup table is left blank. It determines the maximum and the minimum values only when there is at least one non null cell on the map.
### Basic Attributes
Key	Predefined Name	Description
1	“lines”	number of lines
2	“columns”	number of columns
3	“cells”	number of cells (number of lines multiplied by the number of columns)
4	“layers”	number of layers
5	“cellHeight”	cell height (in meters)
6	“cellWidth”	cell width (in meters)
7	“cellArea”	cell area (in hectares)
19	“cellType”	cell type code[1)]
20	“nullValue”	null value1)
[1)] Dinamica EGO 2.0 and above

### Dynamic attributes
Key	Predefined Name	Description
8	“nullCells”	number of null cells
9	“nonNullCells”	number of non null cells
10	“minCell”	minimum value (excluding null cells)
11	“maxCell”	maximum value (excluding null cells)
12	“cellSum”	sum of the values (excluding null cells)

### Statistical attributes
Key	Predefined Name	Description
13	“meanCell”	average (excluding null cells)
14	“cellVar”	variance (excluding null cells)
15	“cellStd”	standard deviation (excluding null cells)
16	“modeCell”	mode (excluding null cells)
17	“medianCell”	median (excluding null cells)
18	“uniqueCells”	total unique occurrences (excluding null cells)

### Cell Type Codes
The codes used to represent all the possible cells types, corresponding to attribute key 19 (“cellType”), are listed below:
Key	Cell Type
0	Unsigned 1 Bit Integer
1	Signed 8 Bit Integer
2	Unsigned 8 Bit Integer
3	Signed 16 Bit Integer
4	Unsigned 16 Bit Integer
5	Signed 32 Bit Integer
6	Unsigned 32 Bit Integer
7	IEEE 754 32 Bit Real

## Internal Name
ExtractMapAttributes