# Rasterize Shape
## Description
This rasterizes a given shape file according to a set of parameters.
## Inputs
Name	Type	Description
Input Shape Filename	Map Filename Type	The filename of the input shape that will be rasterized.
Output Map Filename	Map Filename Type	The filename of the resulting map containing the rasterized shape.

## Optional Inputs
Name	Type	Description	Default Value
Default Output Value	Real Value Type	Default value used to represent all rasterized features from the input shape in the resulting map. Either this value or the “Shape Attribute Name” must be defined, but both can not be defined simultaneously.
Shape Attribute Name	String Type	Name of the shape attribute field used to define the values of the resulting map. Either the attribute name or the “Default Output Value” must be specified, but both can not be defined simultaneously.
Output Map Cell Type	Cell Type Type	Data cell type of the resulting map. For this functor, the cell types Unsigned 1-Bit Integer and Signed 8-Bit Integer are just an alias for cell type Unsigned 8-Bit Integer.	Signed 32-Bit Integer
Output Map Null Value	Null Value Type	Null value of the resulting map.	.default
Output Map Cell Width	Real Value Type	The cell width in the resulting re-projected map. Must be defined together with the cell height. However, the definition of expected cell height/width and number of lines/columns are mutually exclusive. The cell width must be expressed in unit compatible with the projection of the resulting re-projected map.	null
Output Map Cell Height	Real Value Type	The cell height in the resulting re-projected map. Must be defined together with the cell width. However, the definition of expected cell height/width and number of lines/columns are mutually exclusive. The cell height must be expressed in unit compatible with the projection of the resulting re-projected map.	null
Output Map Lines	Positive Integer Value Type	The number of lines expected in the resulting re-projected map. Must be defined together with the number of columns. However, the definition of expected number of lines/columns and cell height/width are mutually exclusive.	null
Output Map Columns	Positive Integer Value Type	The number of columns expected in the resulting re-projected map. Must be defined together with the number of lines. However, the definition of expected number of lines/columns and cell height/width are mutually exclusive.	null
Use Cell Center Only	Boolean Value Type	If true, the interception between lines/polygons and cells is calculated using the cell centers only. Otherwise, all parts of the cells are used. This flag must be set to true, if rasterizing shapes representing linear features (roads, rivers etc)
Use Compression	Boolean Value Type	If true, the resulting re-projected map is compressed. The map compression option only works for GeoTiff (.tif) and HFA (.img) file formats. For other file formats this option is ignored.	true

## Outputs
Name	Type	Description
Output Map Filename	Map Filename Type	The filename of the resulting map. This is the same filename assigned to the corresponding input port.

## Group
GDAL / OGR
## Notes
This functor is basically a wrap around the GDAL library utility GDAL Rasterize.
The resulting map will have the projection and the boundaries of the input shape. The projection and boundaries can be changed using the Transform Map functor.
It is worth noting that, unlike most functors, this functor can not be bound to maps produced by other functors, unless they are saved to the disk first (by using Save Map). Unfortunately, the use of GDAL does not allow us to the use the maps produced by Dinamica EGO while they are still in memory, unless they are re-arranged in a way defined by their API, and such re-arrangement would heavily impact the execution performance and the amount of memory required to perform the re-projection of a map.

## Internal Name
RasterizeMap